## Slide 1: SORPTION AND INCORPORATION OF CAESIUM TO SEDIMENTS AND ILLITE CLAY: A MACRO TO MOLECULAR SCALE INVESTIGATION
Fuller A. J.1,2, Shaw S.1,2, Ward M. B.1, Haigh S. J.2, Mosselmans F. W.3, Peacock C. L.1, Stackhouse S.1, Dent A. J.3, Trivedi D.4, Small J. S.,4 Abrahamsen L. G.4 and Burke I. T.
1University of Leeds
2University of Manchester
3Diamond Light Source Ltd.
4National Nuclear Laboratory Ltd.

## Slide 2: Radiocaesium (137Cs) as a contaminant
High yield fission product (6.3 %)
β,γ decay to 137Ba; t½ = 30.2 years
Very soluble in water as Cs+
Readily taken up by biota
Interacts strongly with soil minerals; esp. clays

## Slide 3: Cs Sorption behaviour
Poinssot et al., GCA, 1999; Bradbury and Baeyens, J. Contam. Hydrol., 2000
Cs sorption to Na Illite (@7 days)
At different Cs concentrations Cs is taken up to different sorption sites

## Slide 4: Three site model of Cs uptake
‘FES’ = Highly selective for Cs; low abundance (<1% of the total CEC)
Type II sites = less selective; greater abundance (~10% CEC)
Planar sites = not selective; very abundant

## Slide 5: Cs sorption to Sellafield type sediment
Cs sorption to Fine grained glacial outwash sand.
1% clay - chlorite & illite/mica
(100 g L-1 @48 hrs)
Fuller et al., Appl. Geochem., 2014
A – @ low Cs concentrations, Cs sorption to FES in competion with K
B – @ intermediate Cs concentrations, sorption to Type II sites in competion with Na & K
C – @ high Cs concentrations, sorption to planar sites / reaches capacity

## Slide 6: pH dependence
Fuller et al., Appl. Geochem., 2014
Discovered that Type II sites are amphoteric in nature (AlOH sites) - used to extended the Bradbury and Baeyeans (2000) cation exchange model for our sediment system
Experiments at different Cs concentrations to probe each type of site independently

## Slide 7: Application to Sellafield GW
Fuller et al., Appl. Geochem., 2014
HLLW
ILLW

## Slide 8: Cs Sorption Kinetics
Comans and Hockley, GCA, 1992
10 ppb Cs+
10mg L-1 Ca-illite
100 mg L-1 Ca-illite
Interaction characterised by rapid uptake period (<1 day) & slower continued uptake (>5 days)
de Koning and Comans, GCA, 2004
Desorption becomes progressively more difficult with time

## Slide 9: Microscopic investigation of Cs sorption on K-illite
Q. Can we visualise Cs sorption and incorporation over time?

## Slide 10: Illite stability in the TEM
Fuller et al., Appl. Clay Sci., 2015
All images collected < 60 seconds

## Slide 11: K exchange with Ca and Cs
K-illite (IMT-1)
20g L-1 in 1 M Cs+/ 0.1 M Ca2+
Bright field TEM images/EDX
Tecnai TF230 FEGTEM, 200KeV
Fuller et al., Appl. Clay Sci., 2015
Investigated the nature of the ‘Frayed Edge’
K → Ca → Cs → Ca

## Slide 12: K → Cs with time
20g L-1 K-illite in 1 M Cs+, HAADF TEM images/EDX, FEI Titan G2, 200 KeV
Fuller et al., Appl. Clay Sci., 2015

## Slide 13: DFT structural modelling
Used the composition of the starting material -
IMT-1 (Mg0.09 Ca0.06 K1.37) [Al2.69 Fe(III)0.76 Fe(II)0.06 Mntr Mg0.43 Ti0.06] [Si6.77 Al1.23]O20(OH)4
to predict expansion expected K → Cs
Approximation | K-Filled | Cs-Filled | Difference
Local Density A. | 0.97 nm | 1.04 nm | 0.064 nm
Generalised Gradient A. | 1.03 nm | 1.09 nm | 0.071 nm
TEM measurements | 1.00 nm | 1.07 | 0.07 nm
DFT model was also used to help predict local co-ordination environment for EXAFS analysis
Fuller et al., Appl. Clay Sci., 2015

## Slide 14: EXAFS analysis
Cs-illite (12 months)
b18 Diamond Light Source
Cs K-edge 35.98 keV
80 K, 12 hrs collection
Athena/Artemis-Feff6.0
Fuller et al., Appl. Clay Sci., 2015
Fit =
12 O atoms @ 3.0-3.4 Å
12 Si(Al) atoms @ 4.0 Å
Good agreement between TEM – DFT – EXAFS

## Slide 15: Conclusions & Implications
Cs initially sorbs to illite at FES site (crystal edge) – can causes interlayer collapse
In time Cs migrates into the interlayer by exchange with K – long term uptake
Cs is held in inner-sphere complex – difficult to exchange out / desorb

## Slide 17: Recent papers from Japan
Mukai et al. 2016, ACS. Use autoradiograghy and TEM to show that Cs (in soil particles) is preferentially sorbed to vermiculated biotite and smectite clay interlayers
Saito et al. 2016, JER. Dialysis resin exchange of Cs from Fukishima soils estimate that the long-term desorption half life is ~2+ years

## Slide 18: HRTEM Cs in Mg Vermiculite
Kogure et al., Chem. Let., 2012; Kikuchi et al., J Min. Pet. Sci, 2015
Mg-vermiculite / K-mica
HAADF image &
Multislice contrast simulation (processed images)
Mg → Cs
Similar interlayer collapse as for illite
Also reported for vermiculated biotite (HAADF images)
Exchange timescales ~25 hours (much quicker than illite)